## Slide 1
THE NATIONAL INSTITUTE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
PROJECT SYNOPSIS
SafeStride Assist
An AI-Based Safe Walking Assistant Using Monocular Depth Estimation
Real-time perception | spatial reasoning | voice feedback
CAMERA
DEPTH + PATH
VOICE ALERT
Batch B15 | Major Project

## Slide 2
SAFESTRIDE ASSIST
OVERVIEW
Abstract
B15 | 02
SafeStride Assist is a research and teaching prototype for safer walking assistance.
It combines YOLO-based detection, ByteTrack tracking, Depth Anything V2, ground-plane calibration, and speech feedback. The central method evaluates a three-metre forward walking corridor instead of reporting every object in the camera view.
The output is a concise action such as: Stop. Path blocked, 2 meters. Keep left. Processing is local by default, and the system is explicitly an educational prototype rather than a certified mobility or emergency device.
PERCEIVE
camera + models
REASON
depth + corridor
GUIDE
voice + captions

## Slide 3
SAFESTRIDE ASSIST
PRESENTATION ROADMAP
Index
B15 | 03
01
Introduction and motivation
02
Problem statement
03
Literature review
04
System architecture
05
System design and data flow
06
Algorithm code snippets
07
Implementation and evaluation
08
Novelty and contribution
09
Limitations and safety
10
Conclusion and references

## Slide 4
SAFESTRIDE ASSIST
MOTIVATION
Introduction
B15 | 04
Assistive technology should reduce uncertainty without removing the user's control.
• Traditional mobility aids remain essential for safe navigation.
• A camera can provide an additional perception channel in unfamiliar environments.
• The useful question is not only what is visible, but what is relevant to the forward path.
• Feedback must be short, prioritised, and understandable under time pressure.
2.0 m
FORWARD CORRIDOR
PATH BLOCKED
Illustrative camera view with a walking corridor and distance-aware blocker

## Slide 5
SAFESTRIDE ASSIST
NEED
Problem statement
B15 | 05
Detection alone is insufficient
• A bounding box does not indicate path relevance.
• A class label does not provide distance or urgency.
• Unknown blockers may not belong to a trained class.
• Frame-by-frame alerts can overwhelm the user.
SafeStride must decide
1
Is the path blocked?
2
How far away is it?
3
Which side is clearer?
4
Should the system speak now?

## Slide 6
SAFESTRIDE ASSIST
RESEARCH FOUNDATION
Literature review
B15 | 06
Real-time detection
YOLO [1]
Fast visual object detection
Temporal tracking
ByteTrack [2]
Stable identities across frames
Monocular depth
Depth Anything V2 [3]
Relative scene-depth estimation
Assistive navigation
Khan, Xu, Eltaher [7, 8, 10]
Navigation and obstacle-avoidance reviews
Multimodal feedback
Katzschmann, Johannesson, Shull [9, 11, 12]
Haptic and audio guidance
User-centred control
Ranganeni, Zhang [13, 14]
Agency and accessible route assistance
Gap addressed: integrate perception, geometry, temporal evidence, risk, and human-centred feedback in one local workflow.

## Slide 7
SAFESTRIDE ASSIST
PROPOSED SYSTEM
System architecture
B15 | 07
The architecture separates sensing, spatial reasoning, decisions, and interaction.
INPUT
IP webcam USB webcam video clip
PERCEPTION
YOLO detection ByteTrack Depth Anything V2
SPATIAL REASONING
Ground plane 3D projection 3 m corridor
DECISION
Risk + TTC priority cooldown
USER OUTPUT
Browser console voice captions
Safety priority
urgent camera obstruction > local path correction > background route/status information
Local processing keeps the core perception loop independent of remote cloud services.

## Slide 8
SAFESTRIDE ASSIST
HOW THE PROTOTYPE WORKS
System design and data flow
B15 | 08
1
Capture
frame
2
Detect + track
objects
3
Estimate depth
geometry
4
Evaluate corridor
path status
5
Rank alert
urgency
6
Speak
guidance
2.0 m
FORWARD CORRIDOR
PATH BLOCKED
STATE
Path: BLOCKED Nearest: 2.0 m Direction: right Advice: KEEP LEFT
VOICE OUTPUT
Stop. Path blocked, 2 meters. Keep left.

## Slide 9
SAFESTRIDE ASSIST
SYSTEM DESIGN DETAIL
Spatial reasoning
B15 | 09
The key design decision is to evaluate the user's forward corridor, not every detected object.
2.0 m
FORWARD CORRIDOR
PATH BLOCKED
Corridor reasoning
• Estimate relative depth with Depth Anything V2.
• Fit a ground plane using the lower image region.
• Project depth into approximate 3D points.
• Evaluate a one-metre-wide corridor up to three metres ahead.
• Mark named or unknown blockers as in_path when geometry supports it.

## Slide 10
SAFESTRIDE ASSIST
IMPLEMENTATION
Code snippets for the algorithms
B15 | 10
CORRIDOR AND DISTANCE
depth = estimate_depth(frame) plane = fit_ground_plane(depth, camera_height) points = project_to_3d(depth, plane) blocked = corridor_has_obstacle( points, width=1.0, max_range=3.0 )
ALERT PRIORITISATION
tracks = bytetrack.update(detections) ttc = estimate_ttc(track_history) priority = rank_alert( in_path, distance, ttc, persistence ) if priority == 'urgent': speak(alert_text)

## Slide 11
SAFESTRIDE ASSIST
PROTOTYPE SCOPE
Implementation and evaluation
B15 | 11
Implemented stack
• Python 3.10+ and PyTorch
• OpenCV and Ultralytics YOLO11s
• ByteTrack and Depth Anything V2
• Browser live console with captions and speech
• IP webcam, USB webcam, uploaded video, or test clip
Evaluation measures
• Precision, recall, and mAP
• Path-blocking accuracy
• Distance-estimation error
• False-alert and missed-hazard rate
• Latency and frames per second

## Slide 12
SAFESTRIDE ASSIST
WHAT IS DIFFERENT
Novelty and contribution
B15 | 12
01
Path-aware perception
Moves beyond object labels by deciding whether the forward walking corridor is blocked.
02
Known and unknown hazards
Combines detector outputs with depth geometry to identify unlabelled blockers.
03
Actionable distance
Turns approximate monocular depth into distance, direction, and side guidance.
04
Safety-first speech
Uses persistence, time-to-collision, priority, and cooldowns to control announcements.

## Slide 13
SAFESTRIDE ASSIST
RESPONSIBLE USE
Limitations and safety boundary
B15 | 13
Known limitations
• Monocular depth is approximate, not guaranteed metric distance.
• Results depend on camera height, pitch, lighting, blur, reflections, crowds, and ground visibility.
• Speech behaviour depends on browser and operating-system audio support.
Safety boundary
• Educational research prototype only.
• Not a certified mobility aid, medical device, or emergency system.
• Must not replace a white cane, guide dog, or human assistance.
• Testing requires supervision and conventional mobility safety methods.

## Slide 14
SAFESTRIDE ASSIST
SUMMARY
Conclusion
B15 | 14
SafeStride Assist demonstrates how perception can become guidance when placed in context.
SEE
detect and track
MEASURE
estimate depth and distance
DECIDE
evaluate path and urgency
SPEAK
give concise guidance
The project provides a modular foundation for future evaluation, calibration, custom hazard models, and accessible navigation research.

## Slide 15
SAFESTRIDE ASSIST
SELECTED SOURCES
References
B15 | 15
[1] Redmon et al., You Only Look Once, CVPR, 2016.
[2] Zhang et al., ByteTrack, ECCV, 2022.
[3] Yang et al., Depth Anything V2, NeurIPS, 2024.
[4] Ranftl et al., Vision Transformers for Dense Prediction, ICCV, 2021.
[5] Ultralytics, Ultralytics YOLO Documentation.
[6] World Health Organization, World Report on Vision, 2019.
[7] Khan et al., Navigation Assistants Systematic Review, IEEE Access, 2021.
[8] Xu et al., Wearable Obstacle Avoidance Travel Aids, IEEE Access, 2023.
[9] Katzschmann et al., Safe Local Navigation with ToF and Haptic Feedback, IEEE TNSRE, 2018.
[10] Eltaher et al., Urban Navigation Systems Review, Sensors, 2021.
[11] Johannesson et al., The Sound of Vision, Brain Sciences, 2016.
[12] Shull and Damian, Haptic Wearables Review, JNER, 2015.
[13] Ranganeni et al., Levels of Control for Blind Travelers, HRI, 2023.
[14] Zhang et al., ARCore User-Centric Assistive Navigation, Applied Sciences, 2019.
Full DOI links and formatted entries are retained in the written synopsis.